## Slide 1: everything

## Slide 2
MAC | IP
End-host
IP: 10.1.2.3
MAC: 11:11:11:11:11
gateway
IP: 10.1.2.1
MAC: 22:22:22:22:22
Google server
IP: 201.1.2.3
MAC | IP
MAC | Interface
MAC | Interface
MAC | Interface
1
3
2
1
2
internet
ARP Table
ARP Table
MAC Forwarding Table
MAC Forwarding Table
MAC Forwarding Table
interface
DNS server
IP: 10.1.2.4
MAC: 33:33:33:33:33
MAC | Interface
MAC Forwarding Table
3
2
1
2
1
DHCP server
IP: 10.1.2.5
MAC: 44:44:44:44:44
It is 6AM, you get to work (the first one there). You open your laptop, connect to ethernet, open a browser and download www.google.com.
Explain which packets were sent and which tables were filled out

## Slide 3
Tcp: syn
Tcp: syn+ack
Tcp: ack
Google server
laptop
Tcp: http: request GET /
Tcp: ack
Tcp: http: reply
Tcp: ack
Get html with URLs to 2 jpeg
Persistent
Non- persistent
Serial
Parallel

## Slide 4
Tcp: syn
Tcp: syn+ack
Tcp: ack
Google server
laptop
Tcp: http: request GET /
Tcp: ack
Tcp: http: reply
Tcp: ack
Get html with URLs to 2 jpeg
Persistent
Non- persistent
Serial
Parallel

## Slide 5
Tcp: syn
Tcp: syn+ack
Tcp: ack
Google server
laptop
Tcp: http: request GET /
Tcp: ack
Tcp: http: reply
Tcp: ack
Get html with URLs to 2 jpeg
Persistent
Non- persistent
Serial
Parallel
Tcp: http: request GET URL of JPEG
Assume jpeg are on the same server
Tcp: ack
Tcp: ack
Tcp: data
Tcp: data
Cwnd=1*MSS
Cwnd=2*MSS
Cwnd=4*MSS
Slow start
Cwnd ++ for each ack

## Slide 6
Non-Persistent serial
Tcp: syn
Tcp: syn+ack
Tcp: ack
Tcp: http: request GET /
Tcp: http: request GET jpeg
Tcp: syn
Tcp: syn+ack
Tcp: ack
Tcp: http: request GET jpeg
Tcp: syn
Tcp: syn+ack
Tcp: ack

## Slide 7
Non-Persistent parallel
Tcp: syn
Tcp: syn+ack
Tcp: ack
Tcp: http: request GET /
Tcp: http: request GET jpeg
Tcp: syn
Tcp: syn+ack
Tcp: ack
Tcp: http: request GET jpeg
Tcp: syn
Tcp: syn+ack
Tcp: ack
url1: pics.google.com/mypic.jpeg
url2: pics.facebook.com/mypic.jpeg

## Slide 8
Your IP & mask == dest IP & mask
Your 128.4.5.1
Dest 128.4.6.1
Mask: 255.255.255.0 dest is not in the same subnet
Mask 255.255.0.0 dest is in the same subnet

## Slide 9
Use DHCP
  Get IP address
  Get subnet mask
  Get gateway IP address (why not include the MAC address? )
  Get DNS server IP address
Get mac address of local dns server
  Broadcast ARP request for MAC address of dns server
  Get reply from DNS server
Get ip address of google
  Send a dns query to local dns server asking for ip address of w.ww.google.com
  Dns server send query to
    Get MAC address of the gateway
    Root server and gets name and ip address of TLD dns server for .com
    TLD for .com and gets name and ip address of google dns servers
    Google dns servers and get ip address of www.google.com
Establish a tcp connection with google
  Send ARP request to get MAC address of gateway
  Send tcp syn to google
  Google send a tcp syn+ack
  Send tcp ack
Send http request to google
  Send tcp message with http request
  Google send tcp ack
Get http reply from google
  Google sends tcp with http reply
  Send a tcp ack
Browser shows the web page

## Slide 10: Basic tasks
It is 6AM, you get to work (the first one there). You open your laptop, connect to Ethernet,
  With DHCP
    get an IP address
    Get subnet mask
    Get gateway ip address
    Get dns server ip address
open a browser and download www.google.com.
  Get IP address of www.google.com
    DNS
    Send DNS query to your local DNS server
    But, before you send a packet to your local DNS server, you need the MAC address of your DNS server
      (how do you know the IP address of the DNS server)
      ARP to find MAC address of local DNS server
        Recall that the link layer switches do not know where the DNS server, and so frames are flooded
    The local DNS server will need to contact other DNS servers to determine the ip address of www.google.com
  Once the IP address of google is known, the browser opens a connection to google
    A TCP SYN packet is constructed and passed to the network layer and then to the MAC layer
    Again, the end host does not know the MAC address of the gateway (which MAC address does it need)
    Once the correct MAC address is known, the MAC layer send the TCP SYN packet
      Maybe the link layer switches need to perform more self-learning
    The google server replies with a TCP-SYN-ACK
    Your host replies with TCP-ACK
    And TCP let’s your browser know that it is connected to google
    The browser makes a HTTP request for file / and host:www.google.com
    The http is given to TCP, which puts it in a TCP packet and send it to google
    The Google server receives the TCP packet and sends a TCP-ACK back
    Google server generated a HTTP reply (let’s assume it fits into one packet) and send it back.
    This reply is given to TCP which sends it to your laptop
    Your laptop gets the tcp packet and sends an ack and gives the http reply to the browser
    The browser gets the message and draws the screen and perhaps requests objects listed in the http reply message

## Slide 11: Basic tasks
It is 6AM, you get to work (the first one there). You open your laptop, connect to ethernet,
  With DHCP
    get an IP address
    Get subnet mask
    Get gateway
    Get dns server
open a browser and download www.google.com.
  Get IP address of www.google.com
    DNS
    Send DNS query to your local DNS server
    But, before you send a packet to your local DNS server, you need the MAC address of your DNS server
      (how do you know the IP address of the DNS server)
      ARP to find MAC address of local DNS server
        Recall that the link layer switches do not know where the DNS server, and so frames are flooded
    The local DNS server will need to contact other DNS servers to determine the ip address of www.google.com
  Once the IP address of google is known, the browser opens a connection to google
    A TCP SYN packet is constructed and passed to the network layer and then to the MAC layer
    Again, the end host does not know the MAC address (which MAC address does it need)
    Once the correct MAC address is known, the MAC layer send the TCP SYN packet
      Maybe the link layer switches need to perform more self-learning
    The google server replies with a TCP-SYN-ACK
    Your host replies with TCP-ACK
    And TCP let’s your browser know that it is connected to google
    The browser makes a HTTP request for file / and host:www.google.com
    The http is given to TCP, which puts it in a TCP packet and send it to google
    The Google server receives the TCP packet and sends a TCP-ACK back
    Google server generated a HTTP reply (let’s assume it fits into one packet) and send it back.
    This reply is given to TCP which sends it to your laptop
    Your laptop gets the tcp packet and sends an ack and gives the http reply to the browser
    The browser gets the message and draws the screen and perhaps requests objects listed in the http reply message

## Slide 12: DHCP
Host generates a UDP message with source port=68 and dest port=67, IP dest=255.255.255.255 (b-cast) and source IP=0.0.0.0
This packet is given to link layer which generates a frame with dest=ff:ff:ff:ff:ff:ff and source=11:11:11:11:11:11
This message is flooded over all switches
  So the switches know a path back to the host
  Any host in the LAN can receive this message, including the DHCP server
    Can a router forward b-cast messages? Discuss?
      E.g., explain ARP if routers forward b-cast messages
        Well, routers could only forward network layer b-casts
      There exists DHCP relays, which allow DHCP messages to be sent between LANs
The DHCP server gets the message and generates a DHCP ACK with contains
  IP address (10.1.2.3)
  IP of local DNS server (10.1.2.4)
  IP of gateway (10.1.2.1)
  Netmask (255.255.255.0)
  This message is sent via UDP with
    source IP = 10.1.2.5
    Dest ip= 255.255.255.255
    Source port=67
    Dest port=68
  The link layer make a frame with source MAC=44:44:44:44:44:44 and dest MAC=11:11:11:11:11:11
    This is smart, usually the dest MAC depends on the dest IP. But here it is different
The link layer switches forward this message directly to the host since the tables know the path to the host
Some switches also know the path back to the DHCP server

## Slide 13
MAC | IP
End-host
IP: 10.1.2.3
MAC: 11:11:11:11:11
gateway
IP: 10.1.2.1
MAC: 22:22:22:22:22
Google server
IP: 201.1.2.3
MAC | IP
MAC | Interface
MAC | Interface
MAC | Interface
1
3
2
1
2
internet
ARP Table
ARP Table
MAC Forwarding Table
MAC Forwarding Table
MAC Forwarding Table
interface
DNS server
IP: 10.1.2.4
MAC: 33:33:33:33:33
MAC | Interface
MAC Forwarding Table
3
2
1
2
1
DHCP server
IP: 10.1.2.5
MAC: 44:44:44:44:44

## Slide 14: Basic tasks
It is 6AM, you get to work (the first one there). You open your laptop, connect to ethernet,
  With DHCP
    get an IP address, Get subnet mask, Get gateway, Get dns server
open a browser and download www.google.com.
  Get IP address of www.google.com
    DNS
    Send DNS query to your local DNS server
    But, before you send a packet to your local DNS server, you need the MAC address of your DNS server
      (how do you know the IP address of the DNS server)
      ARP to find MAC address of local DNS server
        Recall that the link layer switches do not know where the DNS server, and so frames are flooded
    The local DNS server will need to contact other DNS servers to determine the ip address of www.google.com
  Once the IP address of google is known, the browser opens a connection to google
    A TCP SYN packet is constructed and passed to the network layer and then to the MAC layer
    Again, the end host does not know the MAC address (which MAC address does it need)
    Once the correct MAC address is known, the MAC layer send the TCP SYN packet
      Maybe the link layer switches need to perform more self-learning
    The google server replies with a TCP-SYN-ACK
    Your host replies with TCP-ACK
    And TCP let’s your browser know that it is connected to google
    The browser makes a HTTP request for file / and host:www.google.com
    The http is given to TCP, which puts it in a TCP packet and send it to google
    The Google server receives the TCP packet and sends a TCP-ACK back
    Google server generated a HTTP reply (let’s assume it fits into one packet) and send it back.
    This reply is given to TCP which sends it to your laptop
    Your laptop gets the tcp packet and sends an ack and gives the http reply to the browser
    The browser gets the message and draws the screen and perhaps requests objects listed in the http reply message

## Slide 15: DNS
Generate UDP pkt
  DNS request for IP address of www.google.com
  Dest IP = 10.1.2.4
    How did the host learn this?
  Dest port = 53
  Source IP = 10.1.2.3
  Source port = some random value above 1023 and below 2^16
UDP gives packet to network layer which gives it to link layer
First, ARP the DNS server
  Send ARP
    message: whos know the MAC address of 10.1.2.4, tell 10.1.2.3
    Source MAC: 11:11:11:11:11:11
    Dest MAC: ff:ff:ff:ff:ff:ff
    Now, who knows the MAC address for 10.1.2.3?
      Everyone
  Send ARP reply
    The MAC for 10.1.2.4 is 33:33:33:33:33:33
    Dest MAC: 11:11:11:11:11:11
    Source MAC: 33:33:33:33:33:33
    Now who knows the MAC for 10.1.2.4
      Only the host
Once the MAC of the DNS server is known, the DNS request is encapsulated in a ethernet frame with
  Source MAC=11:11:11:11:11:11
  Dest MAC=33:33:33:33:33:33
Do the link layer switches flood with message to the DNS server?
  no, they learned the path to the dns server when the server replied to the ARP
The DNS server does not know the IP of www.google.com. In fact, it does not know any address, except the DNS root
  Send DNS query to root
    For DNS query, UDP pkt with
      Dest port 53, source port random, dest ip=IP of a root DNS server (this is manually entered into the dns server)
    The UDP pkt is given to the network layer
      The network layer looks at the dest ip and sees that the dest in not in this LAN. A table look up determines that the next hop is the gateway which has IP 10.1.2.1
      The link layer needs to get the MAC address for 10.1.2.1
        ARP: who has 10.1.2.1, tell 10.1.2.4
        Source MAC: 33:33:33:33:33:33
        Message is flooded
          So now all machines know the MAC of 10.1.2.4 and all switches know how to reach 33:33:33:33:33:33
        The gateway responds with its MAC

## Slide 16: DNS continue
The DNS server does not know the IP of www.google.com. In fact, it does not know any address, except the DNS root
  Send DNS query to root
    For DNS query, UDP pkt with
      Dest port 53, source port random, dest ip=IP of a root DNS server (this is manually entered into the dns server)
    The UDP pkt is given to the network layer
      The network layer looks at the dest ip and sees that the dest in not in this LAN. A table look up determines that the next hop is the gateway which has IP 10.1.2.1
      The link layer needs to get the MAC address for 10.1.2.1
        ARP: who has 10.1.2.1, tell 10.1.2.4
        Source MAC: 33:33:33:33:33:33
        Message is flooded
          So now all machines know the MAC of 10.1.2.4 and all switches know how to reach 33:33:33:33:33:33
        The gateway responds with its MAC
        The ethernet frame is constructed and sent to the gateway
    The gateway forward this pkt into the internet and it reaches a dns root server, which replies
      It does not know the address of www.google
      But it includes the name of two TLD servers for .com as well as there IP addresses
    This pkt gets to the gateway, which puts the pkt into an ethernet frame with dest 33:33:33:33:33:33
    This frame is send directly to the dns server
  The dns server then sends a dns query to a TLD server
  The TLD server responds with the names of some dns servers of google and the IP addresses of these servers
  The dns server sends a dns query to one of google’s dns servers
  the server replies with the ip address of www.google.com
  The DNS server sends this message to the host

## Slide 17: Basic tasks
It is 6AM, you get to work (the first one there). You open your laptop, connect to wifi,
  With DHCP
    get an IP address, Get subnet mask, Get gateway, Get dns server
open a browser and download www.google.com.
  Get IP address of www.google.com
    DNS
  Once the IP address of google is known, the browser opens a connection to google
    A TCP SYN packet is constructed and passed to the network layer and then to the MAC layer
    Does the host know the MAC address of the gateway?
    No, the end host does not know the MAC address (which MAC address does it need). So ARP is performed
    Once the correct MAC address is known, the MAC layer send the TCP SYN packet
      Maybe the link layer switches need to perform more self-learning
    The google server replies with a TCP-SYN-ACK
    Your host replies with TCP-ACK
    And TCP let’s your browser know that it is connected to google
    The browser makes a HTTP request for file / and host:www.google.com
    The http is given to TCP, which puts it in a TCP packet and send it to google
    The Google server receives the TCP packet and sends a TCP-ACK back
    Google server generated a HTTP reply (let’s assume it fits into one packet) and send it back.
    This reply is given to TCP which sends it to your laptop
    Your laptop gets the tcp packet and sends an ack and gives the http reply to the browser
    The browser gets the message and draws the screen and perhaps requests objects listed in the http reply message