## Slide 1
End-host
IP: 10.1.2.3
MAC: 11:11:11:11:11
gateway
IP: 10.1.2.1
MAC: 22:22:22:22:22
Google server
IP: 201.1.2.3
1
3
2
1
2
internet
interface
DNS server
IP: 10.1.2.4
MAC: 33:33:33:33:33
3
2
1
2
1
DHCP server
IP: 10.1.2.5
MAC: 44:44:44:44:44
It is 6AM, you get to work (the first one there). You open your laptop, connect to ethernet, open a browser and download www.google.com.
Explain which packets were sent in the LAN

## Slide 2: Steps
Configure your laptop
  DHCP
Convert URL (www.google.com) to IP address
  DNS
    ARP
Download web page
  TCP to establish a connection
    ARP
  HTTP request and response

## Slide 3: DHCP
Configures the end-host. Sets end-host’s
  IP address
  Gateway IP address
  Subnet mask
  IP address of (local) DNS server
DHCP Discover
Broadcast UDP pkt to port 68 from port 67
Dest IP = 255.255.255.255
Dest MAC: FF:FF:FF:FF:FF:FF
Source IP: 0.0.0.0
Source Mac: host’s MAC
DHCP Offer
Broadcast UDP pkt to port 67 from port 68
Dest IP = 255.255.255.255
Dest MAC: FF:FF:FF:FF:FF:FF
Source IP: IP of DHCP Server
Source Mac: MAC of DHCP Server
Data: subnet mask + gateway + offered IP
DHCP Request
Broadcast UDP pkt to port 68 from port 67
Dest IP = 255.255.255.255
Dest MAC: FF:FF:FF:FF:FF:FF
Source IP: 0.0.0.0
Source Mac: host’s MAC
Data: requested IP
DHCP Offer
Broadcast UDP pkt to port 67 from port 68
Dest IP = 255.255.255.255
Dest MAC: FF:FF:FF:FF:FF:FF
Source IP: IP of DHCP Server
Source Mac: MAC of DHCP Server
Data: IP, subnet mask, gateway, DNS server, lease time
End-host (e.g., laptop)
DHCP Server

## Slide 4: DHCP: packets sent
End-host send DHCP discovery
DHCP server send DHCP offer
End-host sends DHCP request
DHCP server send DHCP ACK
Packets sent in LAN

## Slide 5: Convert www.google.com to IP Address
DNS (See chapter 2 for details)
  End-host sends DNS query to (local) DNS server
  If nothing is in cache, local DNS server send DNS query to root DNS server
  Root server response with name and IP of TLD
  Local DNS sends DNS query to TLD
  TLD response with name and IP of google DNS servers
  Local DNS sends query to google DNS servers
  Google DNS servers respond with IP of www.google.com
  …
The IP address of (local) DNS server was given by DHCP server

## Slide 6: End-host sends DNS query to (local) DNS server

## Slide 7: End-host sends UDP packet to a destination
DNS application forms a DNS query and gives to the OS
  the data/payload, the destination IP, and destination port
The OS’s transport layer puts the data into a UDP packet and gives the packet to the OS’s network layer
The network layer puts the data into a IP header and gives the packet to the link layer
The link layer needs to make a link layer packet (frame)
  For this, the destination MAC address is needed
  Which destination address is needed?
Application Layer
Transport
Layer
Network
Layer
Link
Layer
Physical
Layer

## Slide 8
Subnet
MAC | IP
End-host
IP: 10.1.2.3
MAC: 11:11:11:11:11
gateway
IP: 10.1.2.1
MAC: 22:22:22:22:22
Google server
IP: 201.1.2.3
MAC | IP
1
3
2
1
2
internet
ARP Table
ARP Table
interface
DNS server
IP: 10.1.2.4
MAC: 33:33:33:33:33
3
2
1
2
1
DHCP server
IP: 10.1.2.5
MAC: 44:44:44:44:44
Can a packet be sent directly to the destination, or must it be sent to the gateway?
Recall: A subnet is a set of hosts that can be reached without going through a router
Objective: Send packet to DNS server
  The DNS server is in the same subnet as the end-host, so packets (frames) can be sent directly to the DNS server
Objective: Send packet to Google server
  Google server is not in the same subnet, so the packet must be sent to the gateway
Details:
  A subnet is defined by an IP address and subnet mask. E.g., 10.1.2.3 and 255.255.255.0
  An IP is in the same subnet as the end host If (end-hosts IP & subnet mask) == (destination & subnet mask)
  (10.1.2.3 & 255.255.255.0) == (10.1.2.4 & 255.255.255.0) is true. The DNS server is in the same subnet as the end-host
  (10.1.2.3 & 255.255.255.0) == (201.1.2.3 & 255.255.255.0) is false. Google server is not in the same subnet as the end-host

## Slide 9: Convert www.google.com to IP Address
The IP address of (local) DNS server was given by DHCP server
DNS (See chapter 2 for details)
  End-host sends DNS query to (local) DNS server
  If nothing is in cache, local DNS server send DNS query to root DNS server
  Root server response with name and IP of TLD
  Local DNS sends DNS query to TLD
  TLD response with name and IP of google DNS servers
  Local DNS sends query to google DNS servers
  Google DNS servers respond with IP of www.google.com
  …
But, no packets can be sent without the MAC addresses

## Slide 10: End-host sends DNS query to (local) DNS server
Since
  (10.1.2.3 & 255.255.255.0) == (10.1.2.4 & 255.255.255.0) is true.
  The DNS server is in the same subnet as the end-host
Conclude: The link layer in the end-host needs the MAC address of the DNS server
From DHCP, we received the IP address of the DNS server. We need the MAC address
  Use ARP

## Slide 11: ARP request
Subnet
End-host
IP: 10.1.2.3
MAC: 11:11:11:11:11
gateway
IP: 10.1.2.1
MAC: 22:22:22:22:22
Google server
IP: 201.1.2.3
1
3
2
1
2
internet
interface
DNS server
IP: 10.1.2.4
MAC: 33:33:33:33:33
3
2
1
2
1
DHCP server
IP: 10.1.2.5
MAC: 44:44:44:44:44
End-host broadcasts an ARP request asking for the MAC address associated with the local DNS server’s IP address
  Request: Who has MAC for IP 10.1.2.4
    Broadcasted to the entire LAN
      Destination MAC: ff:ff:ff:ff:ff:ff
      Source MAC: 11:11:11:11:11:11
  Reply: 33:33:33:33:33 has IP 10.1.2.4
    Sent directly to end-host
      Destination MAC: 11:11:11:11:11:11
      Source MAC: 33:33:33:33:33:33

## Slide 12: End-host uses DNS to convert url www.google.com into an IP address
End-host sends ARP request for MAC of local DNS server
Local DNS server sends ARP reply
End-host sends DNS request to local DNS server
Local DNS server sends DNS query to DNS root server
Packets sent in LAN

## Slide 13: Local DNS server sends DNS query to DNS root server
End-host
IP: 10.1.2.3
MAC: 11:11:11:11:11
gateway
IP: 10.1.2.1
MAC: 22:22:22:22:22
Google server
IP: 201.1.2.3
1
3
2
1
2
internet
interface
DNS server
IP: 10.1.2.4
MAC: 33:33:33:33:33
3
2
1
2
1
DHCP server
IP: 10.1.2.5
MAC: 44:44:44:44:44
Subnet
Local DNS server needs the MAC address of ……..?

## Slide 14: Local DNS server sends DNS query to DNS root server
End-host
IP: 10.1.2.3
MAC: 11:11:11:11:11
gateway
IP: 10.1.2.1
MAC: 22:22:22:22:22
Google server
IP: 201.1.2.3
1
3
2
1
2
internet
interface
DNS server
IP: 10.1.2.4
MAC: 33:33:33:33:33
3
2
1
2
1
DHCP server
IP: 10.1.2.5
MAC: 44:44:44:44:44
Subnet
Local DNS server needs the MAC address of the gateway
Local DNS server sends ARP request for MAC for IP 10.1.2.1
Gateway sends ARP reply

## Slide 15: End-host uses DNS to convert url www.google.com into an IP address
End-host sends ARP request for MAC of local DNS server
Local DNS server sends ARP reply
End-host sends DNS request to local DNS server
Local DNS server sends DNS query to DNS root server
Packets sent in LAN

## Slide 16: End-host uses DNS to convert url www.google.com into an IP address
End-host sends ARP request for MAC of local DNS server
Local DNS server sends ARP reply
End-host sends DNS request to local DNS server
Local DNS server sends ARP request for MAC for IP 10.1.2.1
Gateway send ARP reply to DNS server
Local DNS server sends DNS query to DNS root server
Now the rest of DNS …..
Local DNS server send DNS reply to end-host
Packets sent in LAN

## Slide 17: Basic Steps
Configure your laptop
  DHCP
Convert URL (www.google.com) to IP address
  DNS
    ARP
Download web page
  TCP to establish a connection with google server
    ARP
  HTTP request and response



## Slide 18: TCP to establish a connection with google server
End-host
IP: 10.1.2.3
MAC: 11:11:11:11:11
gateway
IP: 10.1.2.1
MAC: 22:22:22:22:22
Google server
IP: 201.1.2.3
1
3
2
1
2
internet
interface
DNS server
IP: 10.1.2.4
MAC: 33:33:33:33:33
3
2
1
2
1
DHCP server
IP: 10.1.2.5
MAC: 44:44:44:44:44
Subnet
End-host needs the MAC address of the gateway
End-host sends ARP request for MAC for IP 10.1.2.1
Gateway sends ARP reply

## Slide 19: Download web page
End-host send ARP request for MAC for IP 10.1.2.1
Gateway send ARP reply
End-host establishes TCP connection with google server
Packets sent in LAN

## Slide 20: End-host establishes TCP connection with google server
End-host
Google web server
TCP SYN
TCP SYN+ACK
TCP ACK
ACK for SYN+ACK

## Slide 21: Download web page
End-host send ARP request for MAC for IP 10.1.2.1
Gateway send ARP reply
End-host establishes TCP connection with google server
End-host sends TCP SYN packet to google web server
Google web server send TCP SYN+ACK to end-host
End-host sends TCP ACK back to google web server
End host request web page with http
Packets sent in LAN

## Slide 22: End-host establishes TCP connection with google server
End-host
Google web server
TCP SYN
TCP SYN+ACK
TCP ACK
HTTP request
TCP ACK
TCP ACK
HTTP reply
Server working time
}
Web page is displayed

## Slide 23: Download web page
End-host send ARP request for MAC for IP 10.1.2.1
Gateway send ARL reply
End-host establishes TCP connection with google server
End-host sends TCP SYN packet to google web server
Google web server send TCP SYN+ACK to end-host
End-host sends TCP ACK back to google web server
End host request web page with http
Packets sent in LAN

## Slide 24: Download web page
End-host send ARP request for MAC for IP 10.1.2.1
Gateway send ARP reply
End-host sends TCP SYN packet to google web server
Google web server send TCP SYN+ACK to end-host
End-host sends TCP ACK back to google web server
End host request send HTTP request to google web server
  Google web server send TCP ACK
Google web server send HTTP reply with the html file
  End host send TCP ACK
(maybe other web objects are requested and sent)
End host displays web page
Packets sent in LAN

## Slide 25: Download a web page
Configure your laptop
  DHCP
    End-host send DHCP discovery
    DHCP server send DHCP offer
    End-host sends DHCP request
    DHCP server send DHCP ACK
Convert URL (www.google.com) to IP address
  DNS
    ARP
      End-host sends ARP request for MAC of local DNS server
      Local DNS server sends ARP reply
    End-host sends DNS request to local DNS server
    ARP
      Local DNS server sends ARP request for MAC for IP 10.1.2.1
      Gateway send ARP reply to DNS server
    Local DNS server sends DNS query to DNS root server
    Root server replies with name and IP of TLD
    Local DNS send DNS query to TLD
    TLD replies with name and IP of google DNS
    Local DNS send query to google DNS
    Google DNS replies with IP of google web server
    Local DNS send reply to end-host
Download web page
  TCP to establish a connection
    ARP
      End-host send ARP request for MAC for IP 10.1.2.1
      Gateway send ARP reply
    End-host sends TCP SYN packet to google web server
    Google web server send TCP SYN+ACK to end-host
    End-host sends TCP ACK back to google web server
  HTTP request and response
    End host request send HTTP request to google web server
    Google web server send TCP ACK
    Google web server send HTTP reply with the html file
    End host send TCP ACK
    (maybe other web objects are requested and sent)
  End host displays web page
ALL packets sent in LAN
End-host
IP: 10.1.2.3
MAC: 11:11:11:11:11
gateway
IP: 10.1.2.1
MAC: 22:22:22:22:22
Google server
IP: 201.1.2.3
1
3
2
1
2
internet
interface
DNS server
IP: 10.1.2.4
MAC: 33:33:33:33:33
3
2
1
2
1
DHCP server
IP: 10.1.2.5
MAC: 44:44:44:44:44
Subnet